## Slide 1
SAMSUNG PRISM · WORKLET
AI-Native Self-Healing O-RAN Network using a Digital Twin
Aim: an autonomous network-management framework combining AI-based anomaly detection with a digital twin to predict, validate, and resolve RAN faults in a closed loop — for higher reliability, faster recovery, and lower operational effort.
Worklet Objectives
Detect anomalies in O-RAN KPIs via AI-based monitoring
Predict faults before major service disruption
Use a digital twin to validate healing actions safely
Automate corrective actions (tuning, rerouting, recovery)
Compare AI-native vs traditional fault management
Scope of Work
Anomaly detection, root-cause analysis, fault prediction, automated recovery
Twin emulates network states, injects faults, tests mitigations, trains AI on realistic KPIs
Benchmark against rule-based healing
Evaluate under config errors, traffic overload, node/link degradation
Expected Outcomes
Conceptual architecture for AI-native self-healing
Digital-twin testbed for fault injection + recovery validation
AI models for anomaly detection / predictive fault ID
Faster recovery & less downtime vs manual/rule-based
Evaluation gains: availability, recovery time, ops efficiency
TIMELINE
M1 · 0–8 d
Problem study, literature survey, system-architecture design
M2–M3 · 10–22 d
KPI & fault taxonomy; digital-twin setup
M4–M6 · 24–36 d
AI model, healing-logic integration, testing & evaluation
M6 · 40–50 d
Paper & IP draft (publication + patent)
Students: Tanmaya Kumar · Raghu Ram K · Munipalle Jaswanth Kumar Mentors: Bikas Singh (NovaThink Tech) · Navin Kumar

## Slide 2
REVIEW HISTORY
Previous Reviews
Review | Date | Feedback / Comments | Action Taken
Review 1 | — | — | —
Review 2 | — | — | —
Review 3 | — | — | —
Template — fill in the date, mentor/reviewer feedback, and the action taken after each review.

## Slide 3
PROBLEM STATEMENT
Problem Statement
On the O-RAN fronthaul Synchronization (S-) plane: tell a benign timing FAULT from a malicious ATTACK and heal the clock — verified by a digital twin — before the base station fails.
What we are dealing with:
The O-DU–O-RU fronthaul link must stay time-synchronized to ~100 ns (PTP + SyncE); if it drifts, the base station degrades and can fail within ~2 s.
A timing anomaly has two physically different causes that need OPPOSITE responses — a benign fault (GNSS loss / holdover, packet-delay-variation, SyncE degradation) vs a malicious attack (PTP spoofing, replay).
Prior work only DETECTS the anomaly — it does not choose a recovery action, and it cannot separate fault from attack.
A wrong response makes things worse; the correct action must be selected and applied inside the ~2 s failure window.
The healing action must be VERIFIED in a digital twin before it is applied — minimizing wrong-action rate and recovery time (MTTR).

## Slide 4
AI-Native Self-Healing O-RAN Network
Using a Digital Twin for Open-Fronthaul S-plane Recovery
From passive timing telemetry to governed recovery before the ~2 s failure window
CPU-only emulation
Labelled dataset
Hardware-ready path
100 ns
S-plane time-error budget
~2 s
attack-to-failure window
0.547 s
measured governed-loop MTTR
Author: Tanmay | Status: reproducible simulator + benchmark
AI-Native Self-Healing O-RAN S-plane Digital Twin
01
Notes: Open by framing this as the main project made concrete: O-RAN fronthaul, AI-native discrimination, self-healing response, and a digital twin that verifies candidate actions.

## Slide 5
What the Topic Means
Each word maps to a concrete software responsibility, not a slogan.
O-RAN
Open fronthaul
O-DU ↔ O-RU
→
AI-native
learned H0/H1
classification
→
Self-healing
action selection
and rollback
→
Digital twin
counterfactual
verification
Concrete thesis: detect a sync anomaly, separate benign timing faults from malicious attacks, verify recovery actions in a twin, then commit the safest action before the base station fails.
AI-Native Self-Healing O-RAN S-plane Digital Twin
02
Notes: This slide connects the broad title to the narrow research problem. Emphasize that the deck is about the S-plane timing slice of O-RAN.

## Slide 6
Why Fronthaul Timing Matters
PTP + SyncE keep the O-DU and O-RU aligned tightly enough for radio operation.
PTP + SyncE
Open-fronthaul synchronization stack
~100 ns
target time-error class
~2 s
reported crash window under spoofing
O-DU ↔ O-RU
timing domain, not Internet routing
PTP distributes time; SyncE helps frequency stability.
A forged or replayed master can move the slave clock outside budget.
Recovery must be selected before the failure window, not after outage evidence arrives.
AI-Native Self-Healing O-RAN S-plane Digital Twin
03
Notes: Use this slide to make the stakes concrete: this is fronthaul timing security, where nanosecond-scale error can become a base-station outage.

## Slide 7
Where We Sit: The S-Plane
It is not a routing problem and it is not the radio air interface.
Application / SMO
management and orchestration
Near-RT RIC
xApps and policy
O-DU / O-RU fronthaul
C/U/M/S planes
L1/L2 timing
PTP, SyncE, PHC, ESMC
RF air interface
UE and spectrum
Highlighted scope: Open-Fronthaul S-plane
AI-Native Self-Healing O-RAN S-plane Digital Twin
04
Notes: Clarify boundaries: the monitor reads S-plane timing telemetry; later hardware still mostly means timing/networking gear, not SDRs.

## Slide 8
Related Work & The Gap
The gap is action selection and fault-vs-attack separation.
Work
What it does
What remains open
TIMESAFE, ACM ToPS 2025
Shows fronthaul timing attacks and reports a 97.5% detector
Stops at detection; no recovery action; no H0/H1 split
OpenTwin / DTN work
Uses twins for network optimization and data/energy studies
Not focused on S-plane attack recovery
xApp conflict mitigation
Manages conflicting RIC control actions
Different layer; not PTP/SyncE timing
This project
Discriminate H0/H1, verify actions in a twin, commit before failure
Emulated today; hardware validation is next
AI-Native Self-Healing O-RAN S-plane Digital Twin
05
Notes: State the provenance nuance: O-RAN WG11 lists PTP master-clock spoofing as a threat; the 'no comprehensive standard yet' statement comes from research literature assessment, not an official O-RAN quote.

## Slide 9
Problem Statement & Contribution
Contribution: the missing response step plus fault/attack split and a released dataset.
Input
offset, mean path delay, PDV
PTP sequence/message regularity
SyncE QL, GNSS and holdover flags
Decision
detect anomaly
classify H0 benign fault vs H1 attack
forecast each action in the twin
commit only if it beats safe default
Main-topic mapping: O-RAN = fronthaul; AI-native = learned discrimination; self-healing = autonomous action; digital twin = governed verification.
Honest scope: integration + experimental validation + 2,508-window released dataset; not a new fundamental algorithm.
AI-Native Self-Healing O-RAN S-plane Digital Twin
06
Notes: Make the optimization target clear: minimize wrong-action rate and recovery time while staying inside the 100 ns budget and the two-second failure window. This also covers the contribution and honest scope.

## Slide 10
System Architecture
PTP/SyncE
telemetry
Injectors +
dataset
Feature
windows
H0/H1
classifier
Digital twin
forecasts
Governed
healing loop
Action space
+ audit reason
→
→
→
→
↓
→
AI-Native Self-Healing O-RAN S-plane Digital Twin
07
Notes: Walk left to right: the simulator or future hardware feeds telemetry; windows become features; classifier and twin feed the governed action logic.

## Slide 11
Component 1 — S-Plane Simulator
fronthaul_sim/simulator.py
01
A clock-servo model produces PTP/SyncE telemetry on a laptop.
fronthaul_sim/simulator.py
P1 simulator
Key technical terms
PTP offset
mean path delay
PDV
frequency error
SyncE QL
What it does
Disciplines a slave clock
Supports GNSS reference and holdover
Keeps healthy traces within budget
AI-Native Self-Healing O-RAN S-plane Digital Twin
08
Notes: Explain that this is the default realism tier: deterministic pure-Python physics, no PTP NIC required.

## Slide 12
Component 2 — Fault & Attack Injectors
faults/injectors.py
02
Scenario injectors produce timestamped H0, H1, and healthy labels.
faults/injectors.py
P2 labels
Key technical terms
GNSS loss
PDV burst
SyncE degrade
PTP spoof
replay
What it does
Covers three H0 fault modes
Covers two H1 attack modes
Hardening adds overlap and mimicry
AI-Native Self-Healing O-RAN S-plane Digital Twin
09
Notes: Mention realism notes: giveaway labels were removed and attack/fault magnitudes overlap.

## Slide 13
Component 3 — Feature Extraction
telemetry/features.py
03
Sliding windows summarize timing behavior for classification.
telemetry/features.py
10 features
Key technical terms
0.4 s window
0.2 s step
offset stats
sequence regressions
majority label
What it does
Builds ten model inputs
Preserves scenario/run identity
Outputs anomaly labels per window
AI-Native Self-Healing O-RAN S-plane Digital Twin
10
Notes: The feature slide bridges raw simulator traces and the classifier; it explains why decisions can be made inside the two-second window.

## Slide 14
Component 4 — Dataset Builder
dataset/build.py
04
One script assembles telemetry, labelled windows, and the datasheet.
dataset/build.py
2508 windows
Key technical terms
CSV dataset
datasheet
fixed seed
label counts
CPU-only
What it does
1614 healthy windows
536 H0 benign-fault windows
358 H1 attack windows
AI-Native Self-Healing O-RAN S-plane Digital Twin
11
Notes: Read the exact label counts from splane_windows.csv. Emphasize dataset release value for resume and applied research positioning.

## Slide 15
Component 5 — Fault-vs-Attack Discriminator
discriminator/model.py
05
A stratified Random Forest classifies anomalous windows as H0 or H1.
discriminator/model.py
Random Forest
Key technical terms
90 trees
depth 6
65/35 split
ROC-AUC
confusion matrix
What it does
Accuracy 0.987220447284345
ROC-AUC 0.999063829787234
Baseline accuracy 0.3993610223642173
AI-Native Self-Healing O-RAN S-plane Digital Twin
12
Notes: Do not round numbers verbally beyond what the audience can absorb, but the slide uses the measured CSV values.

## Slide 16
Component 6 — Digital Twin
twin/model.py
06
Each candidate action gets a counterfactual time-error trajectory.
twin/model.py
P4 twin
Key technical terms
decay/floor forecast
fidelity score
peak error
steady error
discounted advice
What it does
Ranks candidate recoveries
Reduces trust when telemetry is messy
Keeps safe-default as a comparator
AI-Native Self-Healing O-RAN S-plane Digital Twin
13
Notes: The twin is compact by design. It is a decision support model, not a full hardware emulator.

## Slide 17
Component 7 — Self-Healing Loop
healing/loop.py
07
Detect, classify, verify, and commit with an auditable reason.
healing/loop.py
P5 loop
Key technical terms
safe default
action shortlist
decision budget
audit reason
fallback
What it does
Chooses different actions for H0 vs H1
Checks twin fidelity
Records decision time and reason
AI-Native Self-Healing O-RAN S-plane Digital Twin
14
Notes: Emphasize governance: when fidelity is low, the system falls back rather than blindly automating.

## Slide 18
Component 8 — Benchmark
benchmark/run.py
08
The loop is judged against detection-only, holdover, and failover baselines.
benchmark/run.py
P6 benchmark
Key technical terms
success rate
wrong action
MTTR
peak time error
2 s window
What it does
Governed success 0.95
Wrong-action rate 0.05
Peak error 86.32070997977753 ns
AI-Native Self-Healing O-RAN S-plane Digital Twin
15
Notes: This connects the project contribution to operational value: not detecting attacks, but recovering correctly and quickly.

## Slide 19
Loop Walkthrough (1 / 3): Detect
Each advance adds another stage of evidence.
Detect
offset/PDV over budget
→
Discriminate
H0 fault vs H1 attack
→
Twin-verify
forecast action outcomes
→
Commit / fallback
best action or safe default
The controller does nothing until timing telemetry crosses an anomaly threshold.
AI-Native Self-Healing O-RAN S-plane Digital Twin
16
Notes: Use this as a step-through animation substitute. It is deliberately split across three slides because scripted PowerPoint animations are unreliable.

## Slide 20
Loop Walkthrough (2 / 3): Discriminate
Each advance adds another stage of evidence.
Detect
offset/PDV over budget
→
Discriminate
H0 fault vs H1 attack
→
Twin-verify
forecast action outcomes
→
Commit / fallback
best action or safe default
The response path diverges: benign faults should not be treated like active attackers.
AI-Native Self-Healing O-RAN S-plane Digital Twin
17
Notes: Use this as a step-through animation substitute. It is deliberately split across three slides because scripted PowerPoint animations are unreliable.

## Slide 21
Loop Walkthrough (3 / 3): Verify & Commit
The progressive reveal simulates the motion of the governed control loop.
Detect
offset/PDV over budget
→
Discriminate
H0 fault vs H1 attack
→
Twin-verify
forecast action outcomes
→
Commit / fallback
best action or safe default
The twin compares candidate actions against the conservative safe default; low fidelity triggers fallback.
AI-Native Self-Healing O-RAN S-plane Digital Twin
18
Notes: Use this as a step-through animation substitute. It is deliberately split across three slides because scripted PowerPoint animations are unreliable.

## Slide 22
Results — Discrimination
The classifier beats detection-only while still making real errors.
0.987220447284345
H0/H1 accuracy
0.999063829787234
ROC-AUC for H1
0.9866808510638299
macro F1
0.3993610223642173
detection-only baseline accuracy
Pred H0
Pred H1
True H0
186
2
True H1
2
123
REALISM_NOTES.md: removed message-type giveaways.
Attack and benign-fault magnitudes overlap.
Evasive attacks mimic fault signatures and can occur during congestion.
AI-Native Self-Healing O-RAN S-plane Digital Twin
19
Notes: The prompt asked not to fabricate numbers. These values come directly from discriminator_metrics.csv and REALISM_NOTES.md.

## Slide 23
Results — Self-Healing Benchmark
The measured loop stays inside the 100 ns timing budget and the 2 s failure window.
Method
Recovery
Wrong action
MTTR
Peak error
always failover
0.6
0.0
0.618 s
176.369 ns
always holdover
0.6
0.4
1.18 s
176.369 ns
detection only no response
0.0
0.0
2.0 s
223.827 ns
governed loop
0.95
0.05
0.547 s
86.321 ns
Takeaway
Governed peak error is 86.32070997977753 ns, below the 100 ns budget.
AI-Native Self-Healing O-RAN S-plane Digital Twin
20
Notes: Benchmark values come from benchmark_results.csv. The governed loop is imperfect but materially better than no response and wrong-action-prone simple policies.

## Slide 24
Hardware & Cost — Next Phase
Indicative costs only; verify with vendors before procurement.
Tier A timing lab item
Purpose
Indicative cost
2-3 PCs + PTP NICs
O-DU slave, attacker, load generator
NIC $30-$300 each; reuse PCs
PTP/SyncE-aware switch
Boundary/transparent clock, G.8275.1
$500 budget; $1.5k-$8k telecom
PTP Grandmaster or PC GM + GPSDO
Trusted reference clock
$150-$400 DIY; $2k-$10k appliance
GNSS receiver, antenna, PPS
GNSS-loss and holdover faults
$50-$300
SFPs, cabling, TAP/mirror
Passive PTP capture
$100-$400
Time-error tester
ns-true validation reference
borrow/rent; buy $5k+
Tier A total: DIY/budget ~$800-$3,000 reusing PCs; professional ~$6,000-$18,000.
AI-Native Self-Healing O-RAN S-plane Digital Twin
21
Notes: Key message: because this is S-plane timing, the real testbed is mostly timing Ethernet equipment. A radio is not required to validate the proposed loop.

## Slide 25
Connecting Hardware to Our Software
Same software, real telemetry: linuxptp replaces the simulator input.
PTP GM
GNSS/PPS
Timing-aware
switch
O-DU PC
monitor + loop
Attacker PC
spoof/replay
Optional O-RU
crash demo
↔
↔
↔
↔
Done now
run_all.py reproduction
dataset + benchmark
tests pass 3/3
Next commands
ptp4l / phc2sys / ts2phc
tc netem and packet capture
BMCA allow-list actions
Do not miss
G.8275.1 profile
OCXO vs TCXO holdover
GNSS sky view, PPS skew, UPS
Tier A needs no radio licence
Close: the project is a reproducible response loop today; hardware timestamping is the next validation step.
AI-Native Self-Healing O-RAN S-plane Digital Twin
22
Notes: This final slide combines the connection diagram, practical considerations, done-vs-next status, and closing limitation.