## Slide 1
O-RAN PHY Layer Split
Low PHY (O-RU) vs High PHY (O-DU) — Functional Overview
7.2x Functional Split • Time-critical hardware vs flexible compute

## Slide 2
The Split Logic
One dividing line: latency tolerance
LOW PHY
Lives in the O-RU
Timing: Microseconds
Hardware: FPGA / DSP / ASIC only
Why: Signal-level work closest to the antenna can't tolerate CPU scheduling jitter
7 functions: RE Mapping · FFT/IFFT · Cyclic Prefix · Beamforming · PRACH · DFE · Timing Sync
HIGH PHY
Lives in the O-DU
Timing: Milliseconds
Hardware: CPU / GPU / FPGA
Why: Heavier computation (coding, MIMO math) that can tolerate more flexible processing
9 functions: Channel Coding · Rate Matching · Scrambling · Modulation · Layer Mapping · MIMO Processing · HARQ · Channel Estimation · MIMO Detection

## Slide 3
Low PHY Functions — O-RU
Microsecond-level signal processing, closest to the antenna
Resource Element Mapping
Places data, pilots & control signals into the time-frequency grid
FFT / IFFT Processing
Converts signals between frequency domain and time domain
Cyclic Prefix Processing
Guards against multipath interference between OFDM symbols
Digital Beamforming
Steers radio energy toward a specific user
PRACH Processing
Detects a device's first connection request
Digital Front-End (DFE)
Filtering, interpolation, DPD & CFR before/after RF
Timing Synchronization
Keeps transmitter & receiver aligned in time and frequency

## Slide 4
High PHY Functions — O-DU
Millisecond-tolerant, computationally heavier processing
Channel Coding
Adds redundant bits (LDPC, Polar) to detect & fix errors
Rate Matching
Fits coded bits exactly to the allocated resources
Scrambling
Randomizes the bitstream to avoid long bit runs
Modulation
Converts bits into analog symbols (QPSK to 256-QAM)
Layer Mapping
Spreads symbols across spatial layers for MIMO
MIMO Processing
Spatial multiplexing, diversity & precoding across antennas
HARQ Processing
Smart retransmission of only what's needed
Channel Estimation
Measures channel distortion (LS / MMSE) for decoding
MIMO Detection
Untangles overlapping signals (ZF / MMSE / Sphere)

## Slide 5
Summary: Low PHY vs High PHY
7
Low PHY functions
O-RU · FPGA/DSP/ASIC · microseconds
9
High PHY functions
O-DU · CPU/GPU/FPGA · milliseconds
LOW PHY — O-RU
Function | Timing
RE Mapping | µs
FFT / IFFT | per symbol
Cyclic Prefix | per symbol
Beamforming | per symbol
PRACH Detection | per ms
Digital Front-End | per sample
Timing Sync | continuous
HIGH PHY — O-DU
Function | Timing
Channel Coding | per block (ms)
Rate Matching | per block (ms)
Scrambling | per block (ms)
Modulation | per block (ms)
Layer Mapping | per block (ms)
MIMO Processing | per block (ms)
HARQ | per block (ms)
Channel Estimation | per slot (1ms)
MIMO Detection | per block (ms)