## Slide 1
Notes: Original Samsung PRISM worklet definition, reproduced unchanged. Worklet objective 5 and expected outcome 4 both require comparison against rule-based methods. That requirement is answered on the rule-versus-ML slide. Objectives 2 (prediction) and 4 (automated corrective action) are addressed in the scope-disclosure slide as not yet executed.

## Slide 2
Open Fronthaul S-Plane
Timing Security
Sub-scope of the AI-Native Self-Healing O-RAN Network using a Digital Twin worklet
TEAM
Tanmaya Kumar · Raghu Ram K · Munipalle Jaswanth Kumar
MENTORS
Mr. Bikas Singh (NovaThink Tech)
Dr. Navin Kumar (Amrita Vishwa Vidyapeetham)
Amrita School of Engineering, Bengaluru · Samsung PRISM
168 live on-wire runs · 14 fault scenarios · 12 randomised replicates
Notes: This deck reports the Open Fronthaul S-plane timing-security sub-scope: what was implemented, what data was generated, what was inferred, and what remains. Milestone mapping is retained in the speaker notes of each slide rather than in the visible titles.

## Slide 3
SYSTEM ARCHITECTURE AND PROJECT BOUNDARY
End-to-End O-RAN Architecture and S-Plane Project Boundary
O-RAN Alliance architecture description (ETSI TS 103 982 PAS) | O-RAN.WG4.CUS.0 Control, User and Synchronization Plane Specification | 3GPP TS 38.401 NG-RAN architecture
Notes: Worklet mapping: M1 system architecture design. Sources: O-RAN Alliance, O-RAN Architecture Description (published by ETSI as TS 103 982); O-RAN.WG4.CUS.0 Control, User and Synchronization Plane Specification; 3GPP TS 38.401. Reading order for the audience: the upper row is the O-RAN reference architecture; the lower-left chain is the S-plane timing path (PRTC/grandmaster to boundary clock to O-RU); the highlighted block is the exact region this project worked on; the bottom row is our processing chain from feature extraction to the safe response decision. Note for questions: E2 terminates at O-CU-CP, O-CU-UP, O-DU and O-eNB — it does not reach the O-RU. The project boundary sits on the Open Fronthaul, where E2 does not apply. SyncE is a physical-layer function and was outside this software testbed; only PTP evidence was observed, on the brUP and brDN bridges.

## Slide 4
PROBLEM STUDY
Open Fronthaul Timing Requirements and Security Exposure
O-RAN.WG4.CUS.0 timing categories (via ATIS/WSTS O-RAN Fundamentals tutorial, Armstrong 2022) | ITU-T G.8271.1 network time-error budget | Groen et al., TIMESAFE, ACM ToPS 28(5), 2025, doi:10.1145/3775060
130 ns
Relative time alignment error between radio units in a cluster
Timing Category A; implies ≈±65 ns per O-RU against a common reference under equal allocation
O-RAN.WG4.CUS.0
±1.5 µs
End-application absolute time error, O-RU to primary reference
Total budget at reference point E; the network limit at reference point C is 1100 ns
ITU-T G.8271.1
≈2 s
Observed time from attack onset to O-RU crash in one published study
The O-RU crashed and required a manual reboot, with switch PTP ports in dynamic role
TIMESAFE, ACM ToPS 2025
WHY THIS IS A SECURITY SURFACE, NOT ONLY AN ENGINEERING CONSTRAINT
Time is distributed across the fronthaul as ordinary Ethernet frames carrying the IEEE 1588 protocol, not over a dedicated physical channel. Any device able to place frames on that path can therefore advertise itself as a time source, forge timing content, or withhold legitimate messages. Loss of a shared time reference degrades radio coordination, so the S-plane is simultaneously a timing-performance boundary and an attack surface.
Figure basis
The 130 ns and ±1.5 µs values derive from 3GPP air-interface requirements re-expressed by O-RAN and ITU-T. The ≈2 s figure is a single observed experimental result, not a standardised limit.
Notes: Worklet mapping: M1 problem study. 130 ns is the pairwise relative limit between radio units in a cluster; under equal allocation that implies roughly ±65 ns per O-RU against the common reference, and the fronthaul network receives only a portion of that budget. ITU-T G.8271.1 and G.8272 are paywalled. Values were confirmed against ATIS/WSTS tutorial material and vendor application notes; this is disclosed in the project workbooks. TIMESAFE detail: the failure mode is an O-RU software crash requiring a manual reboot, observed when switch PTP ports were in dynamic role. The same paper's alternative configuration degraded over roughly 580 s.

## Slide 5
DECISION REQUIREMENT
Attack–Fault Ambiguity and Sub-Scope Selection
IEEE 1588-2019 clock states and timePropertiesDS | ITU-T G.8275.1 clockClass ladder (6 locked, 7 holdover in spec) | O-RAN WG11 Threat Model, ETSI TR 104 106 V3.0.0
BENIGN FAULT
The clock is wrong
Example: a GNSS outage at the grandmaster, declared through clockClass 6 → 7.
Correct response — ride it out in holdover.
Isolating the node here creates an outage that was not going to occur.
ATTACK
The clock is wrong
Example: a rogue master injecting false time through forged Announce messages.
Correct response — isolate the source immediately.
Waiting in holdover allows the attacker to keep steering the clock.
Identical observable symptom · opposite correct response · the decision cannot be made from the symptom alone
RATIONALE FOR SELECTING THE S-PLANE SUB-SCOPE
01
Highest consequence
A timing failure can become a service failure within seconds, leaving little time for a safe decision.
02
Genuine ambiguity
Selected benign faults and attacks produce overlapping symptoms; the decision needs provisioned context.
03
Constrained by standards
IEEE 1588-2019 and ITU-T G.8275.1 fix wire-level legality, giving objective decision criteria.
04
Reproducible in software
Real PTP daemons can be executed and attacked on a virtual wire without a proprietary RAN stack.
The sub-scope was selected because it is the point where a detection label alone is insufficient: the same symptom requires opposite recovery actions, and standards supply objective criteria for separating them.
Notes: Worklet mapping: M1 decision requirements and sub-scope definition. Decision parameters used later: allow-listed clock identity, maintenance-window state, clockClass, priority fields, stepsRemoved, sequence continuity, observed message rate, offset, path delay and packet delay variation. If asked why not the whole RAN: scoping to the S-plane is what made rigorous, repeatable measurement possible in the available time.

## Slide 6
LITERATURE SURVEY
Research Foundation for S-Plane Timing Assurance
Groen et al., TIMESAFE, ACM ToPS 28(5), 2025, doi:10.1145/3775060 | Bonati et al., Colosseum, IEEE OJ-COMS, 2024, doi:10.1109/OJCOMS.2024.3447472
Digital Twin for O-RAN, IEEE Communications Magazine, 2024, doi:10.1109/MCOM.003.2400016 | OpenRAN Gym, Computer Networks, 2023 | TSN Digital Twin, EURASIP JIS, 2025, doi:10.1186/s13635-025-00213-7
SOURCE
WHAT THE LITERATURE ESTABLISHES
BOUNDARY LEFT OPEN
TIMESAFE · ACM ToPS 2025
PTP attacks disrupt O-RAN fronthaul and are detectable from packet evidence.
Detection was not tested against a matched set of benign timing faults.
Digital Twin for O-RAN · IEEE 2024
A RAN twin supports testing, optimization and safer control decisions.
The architecture does not validate S-plane attack-versus-fault discrimination.
Colosseum · IEEE 2024
Repeatable Open RAN twins reproduce realistic experimental conditions.
The platform does not address telecom PTP legality or recovery choice.
OpenRAN Gym · Elsevier 2023
O-RAN AI/ML requires controlled data collection and reproducible evaluation.
It does not test whether an S-plane model beats rules or a constant predictor.
TSN Digital Twin · Springer 2025
A timing-aware twin supports structured security testing.
The study does not combine O-RAN PTP, benign lookalikes and held-out controls.
Prior work establishes the threat, the AI testbed direction and the digital-twin direction. It does not resolve the operational decision between malicious timing behaviour and a benign timing fault presenting the same symptom.
Notes: Worklet mapping: M1 literature survey. J. Groen et al., TIMESAFE: Timing Interruption Monitoring and Security Assessment for Fronthaul Environments, ACM Transactions on Privacy and Security 28(5), 2025, DOI 10.1145/3775060. L. Bonati et al., Colosseum: The Open RAN Digital Twin, IEEE Open Journal of the Communications Society, 2024, DOI 10.1109/OJCOMS.2024.3447472. Digital Twin for O-RAN Towards 6G, IEEE Communications Magazine, 2024, DOI 10.1109/MCOM.003.2400016. L. Bonati et al., OpenRAN Gym, Computer Networks, 2023. TSN Digital Twin for STRIDE-Based Security Testing, EURASIP Journal on Information Security, 2025, DOI 10.1186/s13635-025-00213-7. The gap statement is bounded to the locally reviewed source set. It is not a claim that no publication worldwide addresses any part of the problem.

## Slide 7
RESEARCH GAP ANALYSIS
Research Gaps Behind the Experimental Design
Federated Continual Learning for O-RAN Anomaly Detection, IEEE WCNC 2024 | Adversarial ML Threat Analysis in O-RAN, JNCA 2024, doi:10.1016/j.jnca.2024.104090
O-RAN xApps: Survey and Research Challenges, Computer Networks 2025 | Anomaly Detection for xApp and E2 Threats, IEEE 2025
01
Attack and fault ambiguity
Prior detectors separate attack from normal operation. Operators must also separate attacks from real clock, path and configuration faults.
02
Unverified AI claims
Reported model accuracy can appear strong without a held-out split, a rule comparator and a trivial constant baseline.
03
Protocol evidence separated from ML
Standards checks and statistical models are usually presented as alternatives rather than evaluated on the same executed runs.
04
Detection separated from safe response
A label alone does not determine whether to isolate a source, enter holdover or escalate to an operator.
RESULTING STUDY DESIGN
Matched scenarios
Attacks and benign lookalikes execute through the same packet path.
Two decision arms
ARM A applies standards legality plus operator context. ARM B applies Random Forest with an Isolation Forest novelty layer.
Held-out evaluation
Replicates 9–12 remain outside training for the 56-run final test.
Trivial control
An always-BENIGN predictor establishes whether ARM B adds information.
Explicit abstention
Ambiguous evidence escalates instead of forcing an unsafe answer.
Gap addressed: the reviewed source set did not combine S-plane benign lookalikes, standards-aware rules, a machine-learning arm, explicit abstention and a constant baseline within one held-out campaign.
Notes: Worklet mapping: M1 research gap analysis. Federated Continual Learning for Sustainable O-RAN Anomaly Detection, IEEE WCNC 2024. Adversarial Machine Learning Threat Analysis and Remediation in Open Radio Access Network, JNCA 2024, DOI 10.1016/j.jnca.2024.104090. O-RAN xApps: Survey and Research Challenges, Computer Networks 2025. Anomaly Detection for xApp and E2 Interface Threats in O-RAN Near-RT RIC, IEEE 2025. The gap claim is bounded to the reviewed local literature and to the experimental design actually executed.

## Slide 8
CONTRIBUTION POSITIONING
Standards-Grounded Positioning of the Contribution
Normative basis: IEEE 1588-2019, ITU-T G.8275.1, O-RAN.WG4.CUS.0, O-RAN WG11 (ETSI TR 104 106 V3.0.0) | Prior-art boundary: TIMESAFE, Colosseum, OpenRAN Gym, digital-twin literature
01
Normative ground
Protocol legality and telecom timing expectations are taken from recognized standards, not from arbitrary thresholds.
02
Executed evidence
Real PTP daemons, packet captures and daemon telemetry produce auditable observations rather than synthetic rows.
03
Controlled comparison
Rules, machine learning and an always-BENIGN control are scored on the same 56 held-out runs.
04
Governed response
ATTACK, BENIGN and UNKNOWN map to isolation, holdover and escalation policy respectively.
DEMONSTRATED IN THIS CAMPAIGN
Live PTP packet-path execution
Held-out attack and benign-fault classification
ARM A versus ARM B versus constant control
Explicit abstention with evidence provenance
NOT YET DEMONSTRATED
Digital-twin action verification
Executed isolate or holdover recovery
Measured MTTR and availability improvement
An ML model exceeding transparent baselines
Contribution: a standards-aware, controlled S-plane benchmark that tests whether a learned model adds decision value before it is granted authority over recovery.
Notes: Worklet mapping: M1 project justification. This slide separates what was demonstrated from what remains future scope, so that the novelty claim is bounded by executed evidence. Not demonstrated in this campaign: digital-twin orchestration, automatic recovery execution, MTTR reduction, availability improvement.

## Slide 9
STANDARDS FOLLOWED
Telecom Standards and Profile Grounding
Normative basis: IEEE Std 1588-2019 | O-RAN.WG4.CUS.0 | O-RAN WG11 Security Threat Modeling (ETSI TR 104 106 V3.0.0) | ITU-T G.8275.1
Timing performance context: ITU-T G.8273.2 | Frequency synchronization context: ITU-T G.8262 (SyncE, not implemented here)
AUTHORITY
WHAT IT DEFINES
HOW THIS PROJECT USES IT
IEEE 1588-2019
Legal PTP message fields, data sets, clock behaviour and leap-second handling.
ARM A checks field legality, sequence continuity and timePropertiesDS consistency.
O-RAN.WG4.CUS.0
Open Fronthaul C/U/S-plane architecture and synchronization configurations.
Defines the O-DU–O-RU S-plane boundary used by the experiment.
O-RAN WG11
Open Fronthaul threat model, including malicious timing-source behaviour.
Supplies the threat identifiers that label the attack scenarios.
ITU-T G.8275.1
Telecom PTP profile for phase and time distribution with full timing support.
Fixes domain, message rates, transport and the alternate BMCA used by the testbed.
ITU-T G.8273.2
Timing characteristics and limits for telecom boundary clocks.
Provides performance context for interpreting timing-quality evidence.
Scope disclosure
The testbed exercised PTP only; SyncE is a physical-layer function and was not implemented. ITU-T recommendations are paywalled, so several values were confirmed against authoritative secondary sources, as recorded in the project workbooks.
Notes: Worklet mapping: M2 standards grounding. IEEE Std 1588-2019, Precision Clock Synchronization Protocol for Networked Measurement and Control Systems. O-RAN Alliance WG4, Control, User and Synchronization Plane Specification, O-RAN.WG4.CUS.0. O-RAN Alliance WG11, Security Threat Modeling and Risk Assessment, published by ETSI as TR 104 106 V3.0.0 (2025-06). It defines four S-plane threats: T-SPLANE-01 DoS against a master clock; T-SPLANE-02 master impersonation via fake ANNOUNCE; T-SPLANE-03 rogue PTP instance seeking Grand Master; T-SPLANE-04 selective interception and removal of PTP packets. ITU-T G.8275.1, PTP telecom profile for phase/time synchronization with full timing support from the network. ITU-T G.8273.2, Timing characteristics of telecom boundary clocks and telecom time slave clocks. ITU-T G.8262, Timing characteristics of synchronous Ethernet equipment slave clock — cited for context only; SyncE was outside this testbed.

## Slide 10
EXPERIMENTAL CONFIGURATION
Open Fronthaul Timing Testbed Architecture
linuxptp v4.0 (released 2023-06-09), reference implementation of IEEE 1588-2019 and ITU-T G.8275.1 | Linux network namespaces, veth pairs and software bridges | tcpdump packet capture
Six genuine linuxptp 4.0 daemons in isolated Linux network namespaces across two bridged segments. All protocol behaviour — BMCA election, servo control, message cadence — is executed by real daemons, not simulated.
GM-A
grandmaster
GM-B
backup GM
brUP
BC
boundary clock
brDN
RU1
radio unit
RU2
radio unit
RU3
radio unit
CAPTURE AND TELEMETRY
tcpdump on both bridges — every PTP frame recorded unmodified
ptp4l servo logs from all six daemons
pmc management telemetry per run
context.json — ground-truth label plus provisioned operator context
ITU-T G.8275.1 profile as configured
domain 24 · priority1 128 · Sync 16/s (logInterval −4) · Announce 8/s (logInterval −3)
Evidence boundary
No independent clock-error instrument was used; synchronization impact is inferred from protocol and servo telemetry, not measured against a reference clock.
Faults are produced by live packet-path mechanisms — competing daemons, injected frames, replayed captures and link or queue manipulation — never by editing rows in a dataset.
Notes: Worklet mapping: M3 fault-injection testbed (partial — digital twin not exercised). linuxptp 4.0 was released 2023-06-09 and ships configs/G.8275.1.cfg with dataset_comparison G.8275.x. Capture note: PCAPs totalling roughly 222 MB were recorded across the 168 runs. The corrected archive that was packaged for review retains extracted deep CSVs, verdicts, context and scripts, but not the source PCAPs. The absence of an independent clock-error instrument is the reason no conformance claim is made against ITU-T G.8273.2 or G.8271.1.

## Slide 11
CONFIGURATION AND PLATFORM LIMITS
Timing Configuration and Verified Platform Constraints
ITU-T G.8275.1 telecom profile (values cross-checked against Cisco and Nokia profile documentation and linuxptp configs/G.8275.1.cfg) | Constraints confirmed by direct query of the running system
PARAMETER
CONFIGURED VALUE
BASIS
Profile
ITU-T G.8275.1 telecom profile
Full timing support from the network
domainNumber
24
G.8275.1 permitted range 24–43
priority1
128 (fixed)
G.8275.1 fixes the value and the alternate BMCA excludes it from comparison
Sync rate
16 / s (logInterval −4)
G.8275.1
Announce rate
8 / s (logInterval −3)
G.8275.1
BMCA
dataset_comparison G.8275.x
Alternate BMCA, not the IEEE 1588 default
Transport
L2 multicast 01-1B-19-00-00-00
Forwardable address, permitted by G.8275.1 (linuxptp default)
Timestamping
software
Platform limit — see constraints
VERIFIED PLATFORM CONSTRAINTS
!
No PTP hardware clock
ls /dev/ptp* returns empty. Software timestamping only: a microsecond-scale noise floor against a nanosecond-scale target.
!
No loadable kernel modules
modprobe absent and sch_netem unavailable, so congestion uses tbf.
!
One shared oscillator
All namespaces share the host clock, so clocks cannot drift apart.
!
No GNSS receiver
GNSS spoofing and jamming cannot be produced at all.
Effect on scope
These constraints set the ceiling on every result that follows: five of the sixteen catalogued fault classes cannot be produced here, and no claim is made about absolute time-error magnitude.
Every configured value was read back from the running system and traced to the governing standard or, where the normative text is paywalled, to an authoritative secondary source.
Notes: Worklet mapping: M2 KPI configuration and platform constraints. Configuration was verified by reading the live ptp4l configuration of all nine daemon configs, not by restating intended values. Transport note: G.8275.1 permits both 01-1B-19-00-00-00 (forwardable) and 01-80-C2-00-00-0E (link-local). The forwardable address is linuxptp's default and is what this testbed used. This slide is deliberately placed before the results so the evidence ceiling is established first.

## Slide 12
PROCESSING PIPELINE
Data Flow from Packet Capture to Verdict
Deep extractor: 56 fields per PTP frame | Field definitions from IEEE 1588-2019 message and data-set clauses | Conformance flags derived from ITU-T G.8275.1 profile constraints
01
The wire
Real PTP frames produced by six linuxptp daemons on two bridged segments
›
02
Capture
tcpdump records every frame on brUP and brDN, unmodified
›
03
Deep extract
56 protocol and conformance fields per packet; fields that cannot be observed are written EMPTY
›
04
Decision rule
Standards legality plus provisioned operator context, applied as ordered clauses
›
05
Verdict
ATTACK · BENIGN · UNKNOWN, with the triggering clause recorded
INTEGRITY RULE CARRIED THROUGH THE WHOLE PIPELINE
A value that cannot be measured is written EMPTY — never zero.
A zero offset reads as perfect synchronization. An earlier build wrote zero for unobserved fields and consequently reported a blind node as healthy. Nothing is treated as healthy without positive proof of observation, and this rule is applied at extraction, at feature construction and at scoring.
The same extracted evidence feeds both decision arms, so the rule-based and machine-learning comparison is performed on identical executed runs rather than on separately prepared datasets.
Notes: Worklet mapping: M1 system data flow. The 56 columns comprise IEEE 1588 header, flag, correction, identity, sequence and Announce data-set fields, plus derived G.8275.1 conformance flags such as domain legality, multicast legality and message-interval legality. The empty-not-zero rule originated from a real defect found and fixed during development; it is retained as a design constraint.

## Slide 13
DATASET PRODUCED
Experimental Dataset Composition
Packaged archive: splane_campaign_CORRECTED_2026-09-20.tgz, 1096 files, sha256 6149b4fb15940cdac694ba8666d97041b4eb62d5523d2631c1edf96d531e4ed9 | Run inventory enumerated in EVALUATION_V4.json
168
live on-wire runs
14
fault scenarios
12
randomised replicates each
1,451,909
PTP packet records extracted
56
fields per packet
WHAT CONSTITUTES ONE RUN
Two bridge captures
every PTP frame on brUP and brDN, unmodified
One deep-extract CSV
56 fields per packet; unobservable fields written EMPTY
Six daemon servo logs
offset, path delay and frequency per node
One pmc telemetry file
management data set snapshots during the run
One context.json
ground-truth class, fault id, allow-list, maintenance state
Three verdict files
base rule, v2 and v3 scored on the same capture
MEASURABLE AND UNAVAILABLE EVIDENCE
Recorded for every run
Packet header, flag, correction, identity, sequence and Announce data-set fields; derived G.8275.1 conformance flags; per-node servo telemetry.
Structurally unavailable
GNSS status, SyncE quality level, oscillator frequency error and absolute clock error. No hardware exists in this testbed to produce them, so the corresponding columns are EMPTY rather than defaulted.
Partially available
pmc management telemetry is absent for 48 of the 168 runs (all B3, C1, C2 and C3 replicates); this is recorded rather than imputed.
RECORD COUNT VARIES WITH THE FAULT, AND THE VARIATION IS ITSELF EVIDENCE
C1 interception averages 2,360 records per run because the attack starves the link · baseline averages 6,021 · A5 flooding averages 38,319 because the attack adds traffic. Record volume is therefore a discriminating feature, not a data-quality artefact.
Archive contents
Roughly 222 MB of source PCAPs were captured across the campaign. The packaged review archive retains the extracted CSVs, verdicts, context files, daemon logs, scripts and freeze records; it does not retain the source PCAPs.
Notes: Worklet mapping: M3 dataset generation and M6 evidence packaging. Totals recomputed directly from the 168 run directories: 1,451,909 packet records across the downstream extracts; 48,904 daemon log lines; approximately 222.6 MB of PCAP; 499.4 MB total on disk before packaging. Per-scenario mean records per run: A1 7,781; A2 7,655; A3 10,619; A5 38,319; A8 7,858; B2 6,113; B3 5,204; B7 5,834; B_bc_replacement 6,029; B_unplanned_failover 6,102; C1 2,360; C2 5,584; C3 5,506; baseline 6,021. Replicate metadata caveat: 36 C-series context.json files record rep=901; the authoritative replicate number is the one encoded in the run directory name, and the evaluation uses that.

## Slide 14
FAULT INJECTION
Fault Injection Mechanisms on the Live Packet Path
IEEE 1588-2019: message formats, sequenceId continuity, timePropertiesDS §8.2.4, leap-second handling §9.4 | O-RAN WG11 security test identifiers (ETSI TS 104 105) | Scapy, tcpreplay, Linux tc
Additional real PTP daemons
A1 · A8
A new namespace runs a genuine ptp4l instance with an identity outside the provisioned allow-list and a superior data set, then competes for election under the G.8275.1 alternate BMCA. The attack is won on protocol merit, not by editing a capture.
Crafted frame injection
A2 · C2 · C3
Hand-built frames placed on the RU segment: forged two-step timing messages; malformed frames using versionPTP 3, a reserved message type and a short length; Announce frames with leap61 set and the UTC offset falsified.
Capture and replay
A3
tcpdump captures live frames mid-run and tcpreplay retransmits them, producing genuinely stale origin timestamps and reused sequence identifiers rather than synthetic duplicates.
Link and queue manipulation
A5 · C1 · B3 · B7
High-rate flooding; sustained blackholing of the boundary clock's downstream port; a tbf bottleneck carrying competing non-PTP traffic; and bouncing an RU link during a maintenance window.
An attack and its benign twin frequently share the same packet-path mechanism. Killing a grandmaster is identical in B2 and B_unplanned_failover; only the provisioned maintenance context differs. The context is therefore part of the evidence, not metadata.
Notes: Worklet mapping: M3 fault injection on the live packet path. Standards references for the injected conditions: C2 malformed frames map to O-RAN WG11 test 24.2.1.2; C1 interception maps to test 11.1.5.3.1; C3 whole-second abuse concerns IEEE 1588-2019 timePropertiesDS in clause 8.2.4 with leap-second handling in clause 9.4. controlField is deprecated in IEEE 1588-2019 and ignored under G.8275.1, so it is not used as sole legality evidence for C2. sch_netem is unavailable in this kernel, so B3 congestion uses a tbf bottleneck with competing non-PTP background traffic; packets are delayed rather than dropped.

## Slide 15
FAULT TAXONOMY · ATTACK SCENARIOS 1 OF 2
Attack Scenarios: Identity and Message Manipulation
IEEE 1588-2019 Announce, Sync and Follow_Up message clauses and sequenceId continuity | ITU-T G.8275.1 alternate BMCA and message-rate cadence | O-RAN WG11 threat identifiers, ETSI TR 104 106 V3.0.0
SCENARIO
INJECTED CONDITION
OBSERVABLE EFFECT
EXPECTED
RESULT
A1
Rogue grandmaster / BMCA spoof
T-SPLANE-02 / -03
A second real ptp4l instance with an identity outside the provisioned allow-list and a superior priority2 value competes in the election.
The rogue clock wins the alternate BMCA and becomes the advertised time source for the downstream segment.
ATTACK
12/12
correct
A2
Sync / Follow_Up spoofing
IEEE 1588-2019
Forged timing messages from an unallow-listed source identity, sent in bursts, with implausible origin timestamps and no accompanying Announce.
Timing content conflicts with the elected grandmaster while the source never advertises itself legitimately.
ATTACK
12/12
correct
A3
Replay
IEEE 1588-2019 sequenceId
Live frames captured mid-run and retransmitted with tcpreplay, carrying genuinely stale origin timestamps and reused sequence identifiers.
Sequence continuity regresses and timestamps move backwards relative to the active stream.
ATTACK
12/12
correct
A5
DoS / PTP flooding
T-SPLANE-01
High-rate PTP traffic injected on the RU segment in bursts of 300 frames, from a source outside the allow-list.
Message rate far exceeds the profile cadence; record volume rises to roughly 38,000 per run against a baseline of 6,000.
ATTACK
12/12
correct
All four scenarios were detected by the pre-frozen base rule at 12/12, before any rule revision. Detection rests on protocol legality and allow-list membership, not on the magnitude of the timing error produced.
Notes: Worklet mapping: M2 fault taxonomy and M6 per-scenario evaluation. Results shown are for the primary decision rule and are identical to the pre-frozen base rule on these four scenarios. ETSI TR 104 106 V3.0.0 defines four S-plane threats. A1 maps to T-SPLANE-02 and -03; A5 maps to T-SPLANE-01. A3 replay has no direct counterpart in that set, which is stated rather than forced.

## Slide 16
FAULT TAXONOMY · ATTACK SCENARIOS 2 OF 2
Attack Scenarios: Relay, Interception and Field Abuse
O-RAN WG11 security test identifiers 11.1.5.3.1 and 24.2.1.2 (ETSI TS 104 105) | IEEE 1588-2019 stepsRemoved, timePropertiesDS §8.2.4 and leap-second handling §9.4 | ETSI TR 104 106 V3.0.0
SCENARIO
INJECTED CONDITION
OBSERVABLE EFFECT
EXPECTED
RESULT
A8
Rogue boundary clock
T-SPLANE-03
A two-port ptp4l instance slaves to the legitimate grandmaster upstream and re-advertises downstream with stepsRemoved incremented.
An unauthorised clock is inserted into the timing path while still relaying genuine time, so content alone appears valid.
ATTACK
12/12
correct
C1
Selective interception and removal
T-SPLANE-04
The boundary clock's downstream port is blackholed for a sustained fraction of the observation window, withholding Sync and Announce.
Radio units receive messages below the rate the boundary clock itself declares; delivered-to-declared ratio falls toward 0.37.
ATTACK
11/12
correct
C2
Malformed / fuzzed frames
WG11 24.2.1.2
Frames injected with versionPTP 3, a reserved message type, and a message length shorter than the protocol permits.
Frames are structurally illegal under IEEE 1588-2019 regardless of their timing content.
ATTACK
12/12
correct
C3
Whole-second field abuse
IEEE 1588-2019 §8.2.4
Announce frames carrying leap61 asserted, currentUtcOffset falsified to 0 against a true value of 37, and traceability flags stripped.
Time properties become internally inconsistent, which would shift the applied UTC offset by a whole second.
ATTACK
12/12
correct
Note
The pre-frozen base rule returned BENIGN on C1, C2 and C3 at 0/12 each. These three coverage gaps were closed by a disclosed post-campaign rule revision, evaluated on the same captures and reported separately from the pre-frozen result.
Notes: Worklet mapping: M2 fault taxonomy and M6 per-scenario evaluation. C-series scenarios are campaign identifiers derived from O-RAN WG11 test cases, not A/B taxonomy classes. C1 result is 11/12: one replicate at a 60 percent blackhole evaded the detector. This is quantified on the detection-boundary slide. controlField was historically used as a legality signal for malformed frames but is deprecated in IEEE 1588-2019 and ignored under G.8275.1, so it is not relied on.

## Slide 17
FAULT TAXONOMY · BENIGN SCENARIOS
Benign Fault and Operational-Change Scenarios
ITU-T G.8275.1 clockClass ladder and stepsRemoved semantics | IEEE 1588-2019 BMCA re-election behaviour | Provisioned operator context: allow-list, maintenance-window state, expected boundary-clock identity
SCENARIO
INJECTED CONDITION
OBSERVABLE EFFECT
EXPECTED
RESULT
baseline
Healthy control
—
All six daemons nominal: grandmaster A elected, relayed through the boundary clock to three radio units.
Stable offset and path delay; message cadence matches the declared profile rates.
BENIGN
12/12
correct
B2
Planned grandmaster changeover
ITU-T G.8275.1
Grandmaster A withdrawn during an open maintenance window; grandmaster B, which is on the provisioned allow-list, is elected.
A grandmaster change identical in packet terms to A1 — the distinguishing evidence is allow-list membership plus maintenance state.
BENIGN
12/12
correct
B3
Packet delay variation and congestion
ITU-T G.8261
A 1 Mbit tbf bottleneck on the boundary-clock to radio-unit path carrying competing non-PTP background traffic.
Real queueing delay: Sync packet delay variation rises from 0.07 ms to between 5.6 and 857 ms, with no packet loss and no protocol anomaly.
BENIGN
11/12
correct
B7
Topology reconfiguration
IEEE 1588-2019
A radio-unit link is bounced and re-homed during an open maintenance window.
stepsRemoved and measured path delay change consistently with the new topology, with no illegal field values.
BENIGN
12/12
correct
B_bc_repl
Planned boundary-clock replacement
ITU-T G.8275.1
A provisioned replacement boundary clock is swapped in during maintenance; its identity is recorded in the operator context.
A new clock identity appears in the timing path relaying the genuine grandmaster — structurally identical to the A8 rogue relay.
BENIGN
0/12
open failure
Note
Four of five benign scenarios were classified correctly. The boundary-clock replacement is the single systematic failure: the decision context carries one expected boundary-clock identity, so a legitimate replacement is read as an unauthorised relay.
Notes: Worklet mapping: M2 fault taxonomy and M6 per-scenario evaluation. B3 records 11 of 12 correct. The single incorrect run returns UNKNOWN, not ATTACK — it is an over-cautious abstention under severe congestion, not a false alarm. B_bc_replacement produces 12 false ATTACK calls and is the dominant cause of the 0.783 macro specificity. Excluding it, benign classification is 47 of 48, or 0.979. B3 was rebuilt after an audit found the original netem-based injection never executed; the corrected scenario uses a tbf bottleneck with competing traffic.

## Slide 18
FAULT TAXONOMY · AMBIGUOUS CASE AND COVERAGE
Ambiguous Scenario and Catalogue Coverage
Sixteen-class S-plane fault catalogue maintained in the project parameter matrix (144 parameters × 16 fault classes) | Threat identifiers from ETSI TR 104 106 V3.0.0 | Coverage assessed against verified platform constraints
B_unplanned_failover · DELIBERATELY AMBIGUOUS
Grandmaster A fails with no maintenance window open; provisioned grandmaster B is elected.
From packet evidence alone this is indistinguishable from an attack that suppressed the grandmaster. Both produce an unplanned election to a legitimate backup. The decision rule returns UNKNOWN and escalates rather than forcing a binary answer.
EXPECTED UNKNOWN
12 / 12 correct
Abstention is scored on its own axis, not as a detection success.
SIXTEEN-CLASS CATALOGUE COVERAGE
A1
SW
TESTED
Rogue grandmaster / BMCA spoof
A2
SW
TESTED
Sync / Follow_Up spoofing
A3
SW
TESTED
Replay
A4
SW*
not run
Delay (time) attack
A5
SW
TESTED
DoS / PTP flooding
A6
HW
blocked
GNSS spoofing
A7
HW
blocked
GNSS jamming
A8
SW*
TESTED
Rogue boundary clock
B1
HW
blocked
GNSS holdover
B2
SW
TESTED
Planned GM changeover
B3
SW
TESTED
PDV / congestion
B4
HW
blocked
SyncE / EEC degradation
B5
SW*
not run
Static path asymmetry
B6
HW
blocked
Oscillator drift
B7
SW
TESTED
Topology reconfiguration
B8
SW
not run
Measurement noise floor
Eight of sixteen catalogued classes were executed. Five require physical timing hardware and cannot be produced here. Three have software detection logic only, where physical impact would need hardware to measure. SW* denotes detection logic without physical-impact measurement.
Notes: Worklet mapping: M2 fault taxonomy and coverage statement. Catalogue tally from the project parameter matrix: eight fully-software classes (A1, A2, A3, A5, B2, B3, B7, B8); three software-detection-only classes (A4, A8, B5); five hardware-required classes (A6, A7, B1, B4, B6). ETSI mapping is partial and stated as such: A5 to T-SPLANE-01, A1 to T-SPLANE-02 and -03, A8 to T-SPLANE-03, C1 to T-SPLANE-04. Replay, delay attack and the GNSS classes have no direct counterpart among the four defined S-plane threats. The three C-series scenarios are campaign identifiers derived from O-RAN WG11 test cases; they sit alongside this catalogue rather than inside it.

## Slide 19
CLASSIFICATION METHOD
Classification Logic and Verdict Assignment
IEEE 1588-2019 field legality, data-set consistency and sequence continuity | ITU-T G.8275.1 profile constraints and clockClass ladder | Provisioned operator context supplied per run in context.json
BENIGN FAULT SIGNATURE
Degradation that is self-consistent with a declared, standards-compliant state change: clockClass 6 to 7 for a grandmaster entering holdover within specification, stepsRemoved changing consistently with a new topology, or delay variation rising without any field becoming illegal.
The declaration and the observation agree.
ATTACK SIGNATURE
Evidence that is illegal or unauthorised: forged Announce fields, non-monotonic sequence identifiers, structurally invalid frames, a delivered message rate below the rate the source itself declares, or a superior clock whose identity is outside the provisioned allow-list.
The declaration and the observation disagree.
VERDICT ASSIGNMENT AND RECOMMENDED RESPONSE
ATTACK
Protocol-inconsistent or unauthorised evidence present
ISOLATE
BENIGN
Only provisioned clocks, no legality violation
TOLERATE / HOLDOVER
UNKNOWN
Packet evidence cannot distinguish intent
ESCALATE
Recommended response labels only. No corrective action was executed on this testbed.
The worked discriminator: a grandmaster suddenly changes. It could be B2, a planned failover, or A1, BMCA spoofing. The decisive test is whether the new clock identity appears on the provisioned allow-list and whether a maintenance window is open. Both scenarios were classified correctly at 12/12.
On the deliberately ambiguous unplanned failover the rule returned UNKNOWN on 12 of 12 runs. A BENIGN call there would be an unsafe over-claim and an ATTACK call a false alarm; both are treated as failures.
Notes: Worklet mapping: M5 decision engine, partial — classification evaluated, closed-loop healing not validated. Classification tests self-consistency against the standard and against provisioned intent. It does not react to the magnitude of the timing error. The rule is expressed as ordered clauses, and the triggering clause is recorded with every verdict so that each decision is auditable. ISOLATE, TOLERATE/HOLDOVER and ESCALATE are verdict outputs. No isolation, holdover entry or escalation was executed or measured.

## Slide 20
EXPERIMENT DESIGN
Campaign Design and Reproducibility Controls
Decision rule SHA-256 hashed before execution (FROZEN.json) | Per-replicate randomisation seeded from the replicate number | Pre-registered expected verdicts | Full run inventory in EVALUATION_V4.json
168
live on-wire runs
14
scenarios
12
randomised replicates each
3
rules scored on identical captures
Rule frozen before execution
The base decision rule was SHA-256 hashed before any run started, so it could not be tuned to the outcome. The hash is recorded in the packaged archive.
Revision history disclosed
Rule v3 was written after v2 false positives were observed, then re-hashed before scoring. It is reported as a transparent post-observation revision, not as independent validation.
Pre-registered expectations
Each scenario's expected verdict was written down in advance. Sensitivity, specificity and abstention are scored on separate axes rather than pooled into one figure.
Per-replicate randomisation
Attacker identity, priority, burst size, inter-frame gap and onset are drawn reproducibly from the replicate number, so repeats test generalisation rather than repetition.
Per-scenario reporting
Per-scenario recall is the primary metric. Pooled figures move with how many runs of each scenario exist, so they are labelled descriptive only.
Design limit
The three C-series scenarios draw from only four to five distinct randomised parameter values, so twelve replicates are twelve genuine captures but not twelve independent attack designs.
Notes: Worklet mapping: M6 campaign design and reproducibility controls. Base rule hash c362e11…; v3 hash aa9417b7…. v2 and v3 produce identical verdicts on all 168 runs, verified per run. Additive-only verification was performed per run rather than by comparing summary scalars: zero runs exist where the base rule said ATTACK and v3 did not; 35 escalations occur, all on C1, C2 and C3.

## Slide 21
EXPERIMENTAL INTEGRITY
Pipeline Audit and Corrective Reruns
Independent audit of the campaign apparatus, 2026-09-20 | Defect evidence and corrective actions recorded in AUDIT_AND_CORRECTIONS | All affected runs re-executed before any result in this deck was computed
A cross-check audit of the campaign apparatus identified four defects. Two of them had produced invalid data. Every affected run was re-executed, and the results reported later in this deck are computed only from the corrected campaign.
Thirty-six replicates were three captures copied twelve times
A runner script was created without the execute bit. The resulting exit code 126 was silenced by output redirection, and a stale capture then satisfied the packet-count validity guard.
Proof: one distinct SHA-256 across twelve supposed replicates, and completion in under one second where a genuine run takes about 48 seconds.
FIXED · re-run
A benign scenario never injected anything
This kernel has no sch_netem qdisc, and the failure was swallowed by a shell fallback. B3 congestion was a baseline run carrying a congestion label.
Proof: B3 packet delay variation was statistically identical to baseline and to the untouched control node. Rebuilt with a tbf bottleneck and competing traffic.
FIXED · rebuilt
A detector produced false positives on upstream captures
Rule v2's rate-starvation clause had no minimum-sample or transient guard, so a boundary clock emitting three frames during BMCA start-up read as rate-starved.
Effect: it turned a benign failover into an ATTACK and destroyed a correct abstention. Rule v3 adds a minimum-frame floor and a persistence requirement.
FIXED · v3
The evaluator overstated and under-checked
Pooled metrics moved with run count, additive-only behaviour was asserted by comparing two scalars, abstention was credited on error paths, and attribution scoring was dropped.
Replaced with a per-scenario evaluator applying macro averages, per-run additive-only verification and an explicit replicate whitelist.
REPLACED
Disclosing defects found in our own pipeline is treated as part of the experimental result. Two of the four had fabricated data; both were corrected and re-executed, and the withdrawn figures are not reported anywhere in this deck.
Notes: Worklet mapping: M6 experimental integrity. The audit also found that run/randparams.py and run/scenarios.sh no longer match the original frozen manifest. That change is disclosed in FROZEN_HARNESS_EPOCH2.json. The decision rules themselves are unchanged and still match their original hashes — only the experiment apparatus changed. An earlier 132-run campaign is superseded by this corrected 168-run campaign. The B3 defect also invalidates B3 in that earlier campaign, so its figures are withdrawn and are not presented.

## Slide 22
CLASSIFICATION RESULTS
Scenario-Level Classification Results
168 live runs, 14 scenarios, 12 replicates each | Wilson score 95% confidence intervals | Expected verdicts pre-registered before execution | Source: EVALUATION_V4.json
SCENARIO
EXPECTED
PRE-FROZEN BASE RULE
REVISED RULE v3
95% CI (v3)
A1 rogue grandmaster
ATTACK
12/12
12/12
0.757–1.000
A2 Sync spoofing
ATTACK
12/12
12/12
0.757–1.000
A3 replay
ATTACK
12/12
12/12
0.757–1.000
A5 DoS flooding
ATTACK
12/12
12/12
0.757–1.000
A8 rogue boundary clock
ATTACK
12/12
12/12
0.757–1.000
C1 selective interception
ATTACK
0/12
11/12
0.646–0.985
gap closed
C2 malformed frames
ATTACK
0/12
12/12
0.757–1.000
gap closed
C3 whole-second abuse
ATTACK
0/12
12/12
0.757–1.000
gap closed
baseline
BENIGN
12/12
12/12
0.757–1.000
B2 planned GM changeover
BENIGN
12/12
12/12
0.757–1.000
B3 congestion
BENIGN
11/12
11/12
0.646–0.985
1 abstention
B7 topology reconfiguration
BENIGN
12/12
12/12
0.757–1.000
B_bc_replacement
BENIGN
0/12
0/12
0.000–0.242
open failure
B_unplanned_failover
UNKNOWN
12/12
12/12
0.757–1.000
Per-scenario recall is the primary metric. Three coverage gaps — interception, malformed frames and whole-second abuse — moved from 0/12 to 11/12, 12/12 and 12/12 with no change in benign performance. One benign scenario remains an open failure.
Notes: Worklet mapping: M6 per-scenario evaluation. Intervals are Wilson score 95% intervals computed on n=12 per scenario; they are wide by construction at that sample size. The B3 incorrect run returns UNKNOWN rather than ATTACK, so it is an abstention on a benign scenario, not a false alarm. B_bc_replacement produces 12 false ATTACK calls. All counts were recomputed directly from the 168 run directories rather than read from a summary file.

## Slide 23
CLASSIFICATION RESULTS
Aggregate Classification Performance
Macro averages over per-scenario correctness rates, 168 live runs | Attack sensitivity over 8 attack scenarios, specificity over 5 benign scenarios, abstention over 1 ambiguous scenario | Source: EVALUATION_V4.json
0.990
Macro attack sensitivity
revised rule v3 · pre-frozen base rule 0.625 on the same captures
0.783
Macro benign specificity
identical for both rules, so the revision introduced no regression
1.000
Abstention correctness
ambiguous unplanned failover returned UNKNOWN on 12 of 12 runs
0.875
Fault attribution accuracy
84 of 96 attack runs had the specific fault correctly named
WHAT IMPROVED
The revised rule closed three coverage gaps on the same captures: selective interception 0/12 to 11/12, malformed frames 0/12 to 12/12, and whole-second abuse 0/12 to 12/12. Benign performance is unchanged, and per-run verification confirms zero regressions — no run that the base rule called ATTACK was downgraded.
WHY SPECIFICITY IS 0.783 AND NOT 1.000
Two benign scenarios miss. B_bc_replacement produces 12 false ATTACK calls and is the dominant cause. B3 congestion contributes one UNKNOWN. Excluding the boundary-clock replacement, benign classification is 47 of 48, or 0.979 — so the loss is one identified systematic gap plus one cautious abstention, not diffuse error.
Reporting integrity
The 0.990 figure belongs to the post-observation revised rule. The pre-frozen base rule scored 0.625 on the same captures. Both are shown so the improvement is not mistaken for independent pre-registered validation.
Headline position: strong attack detection with one identified and explainable benign failure, an honest abstention on the genuinely undecidable case, and correct fault attribution on seven of eight attack scenarios.
Notes: Worklet mapping: M6 primary results. Macro sensitivity 0.9896 rounds to 0.990. Macro specificity is 0.7833. Attribution is 84 of 96 attack runs with a Wilson interval of 0.794 to 0.927. Because every scenario has n=12, the macro averages coincide numerically with pooled rates here; they are still reported as macro figures because pooled rates move with run counts in general.

## Slide 24
RULE-BASED AND ML COMPARISON
Rule-Based and Machine-Learning Classification Compared
Worklet objective 5 requires comparison against traditional fault management | Session-disjoint split: trained on replicates 1–8, tested on replicates 9–12 (56 held-out runs) | Hyperparameters and split fixed before scoring
ARM A · RULE-BASED
Frozen decision rule
Inputs: 56 extracted packet fields plus provisioned operator context. No training. SHA-256 frozen before the campaign; v3 is a disclosed post-campaign revision.
ARM B · MACHINE LEARNING
Random Forest + Isolation Forest
90 trees, depth 6, balanced classes, seed 1588, with an Isolation Forest novelty layer for abstention. Inputs: ptp4l servo telemetry only — offset, path delay and delay variation.
CONTROL · ALWAYS-BENIGN
Constant predictor
Returns BENIGN for every run. Included so that any apparent ML skill can be tested against the trivial baseline rather than assumed.
METRIC ON 56 HELD-OUT RUNS
ARM A — RULE
ARM B — ML
ALWAYS-BENIGN
Exact accuracy
51/56 (0.911)
24/56 (0.429)
20/56 (0.357)
Attack sensitivity
0.969 (31/32)
0.156 (5/32)
0.000 (0/32)
Benign specificity
0.800 (16/20)
0.950 (19/20)
1.000 (20/20)
Correct abstention
1.000 (4/4)
0.000 (0/4)
0.000 (0/4)
ARM B IS NOT DISTINGUISHABLE FROM THE CONSTANT PREDICTOR
ARM B returns BENIGN on 47 of 56 runs and improves on the constant predictor by four runs. A paired exact McNemar test gives p = 0.219, so the difference is not significant at this sample size. Both score 4/4 on the boundary-clock replacement, so that result is not a unique learned capability.
NO MEASURED COMBINATION EXCEEDS THE RULE ARM
Combining the arms was evaluated rather than assumed. Logical OR reaches 0.893, rule-first with ML fallback 0.839, and consensus-else-abstain 0.429. All fall below ARM A at 0.911, so no combination is recommended on this evidence.
Scope condition
ARM B operated on 6 of 28 configured features because GNSS, SyncE, oscillator and protocol-legality telemetry do not exist in this testbed. This is a result about the available observability, not a general verdict on machine learning.
Notes: Worklet mapping: M4 model development and M6 objective-5 comparison. The split is session-disjoint by replicate, never by window, so no window from a test run appears in training. Per-window figures reported separately: ARM B window accuracy 0.544 and ROC-AUC 0.604 over 1,923 windows on known scenarios. These are window-level, not run-level, and are not comparable with the run counts in the table. McNemar exact two-sided p = 0.21875 from 5 discordant pairs favouring ARM B against 1 favouring the control.

## Slide 25
RESULT INTERPRETATION
Observability Constraints Behind the ML Result
Feature availability derived from observed linuxptp servo provenance | Schema defaults and synthetic parser fields invalidated to NaN before fitting | Impurity-based feature importances from the fitted Random Forest
The machine-learning arm underperformed because of what this testbed can observe, not because the method is unsuited to the problem. Three measured constraints account for the result.
01
Only 6 of 28 configured features carried data
GNSS status, SyncE quality, oscillator error and every protocol-legality feature are absent from ptp4l servo logs. The model could key only on offset, path-delay and delay-variation magnitude — and one of the six, holdover rate, had zero importance, so five features carried all the signal.
02
Two attacks starve the very telemetry the model needs
Servo samples average 88.0 per baseline run, falling to 44.5 for selective interception and 28.0 for whole-second abuse. An attack that suppresses timing messages also suppresses the evidence a telemetry-based detector depends on. The rule arm is unaffected because it reads packet legality and rate deficit directly.
03
Importances indicate testbed-servo artefact risk
Ranked importances are offset_abs_max 0.268, path_delay_mean 0.262, offset_std 0.208, pdv_std 0.139 and offset_mean 0.124 — all timing magnitude and dispersion, none protocol semantics. With a single testbed, domain shift cannot be separated from intrinsic class overlap.
Evidence-based conclusion: on this telemetry the rule arm is the correct operational choice. Starvation alone does not explain the result — ARM B also fails on attacks where servo telemetry is intact — so feature poverty and class overlap are the primary causes. A fair re-test requires richer management-plane telemetry, not a different classifier.
This is an argument for retaining a standards-aware rule layer and for improving observability before granting a learned model authority over recovery. It is not a claim that machine learning is inherently unsuited to S-plane timing security.
Notes: Worklet mapping: M6 objective-5 interpretation. The sparsity asymmetry is the most transferable architectural finding: attacks that starve telemetry blind a telemetry-based detector but not a packet-based one. Because ARM B's attack sensitivity is 0.156 across all eight attack scenarios, including A1, A2, A3, A5 and A8 where servo telemetry is intact at roughly 88 lines per run, starvation on C1 and C3 compounds the problem rather than causing it.

## Slide 26
UNRESOLVED CASES
Measured Detection Boundary of the Interception Detector
Rate-starvation clause fires when the delivered message rate falls below half the rate the source itself declares | Blackhole fraction drawn per replicate from randparams.py | Ratios recomputed from the per-run deep extracts
Selective interception is the one attack scenario that is not detected on every replicate. The miss is precisely located rather than described as residual error.
CONFIGURED BLACKHOLE FRACTION OF THE POST-WARM-UP INJECTION WINDOW
REPLICATES
DELIVERED / DECLARED RATE
OUTCOME
75 %
n = 6
0.3665
CAUGHT
70 %
n = 3
0.4137
CAUGHT
65 %
n = 2
0.4581 / 0.4619
CAUGHT
60 %
n = 1
0.5049
MISSED
Detection threshold · delivered / declared < 0.500
At 60 % the ratio is 0.5049 — 0.0049 absolute, or 0.98 % relative, above the threshold. The attack evades by a margin of five parts in a thousand.
WHAT WAS MEASURED AND WHAT WAS INTERPOLATED
Measured: 65 % is caught, 60 % is missed. The tested bracket is therefore 60–65 %. Linear interpolation of the delivered-to-declared ratio across that bracket places the crossing at approximately 60.5 %. That crossing is interpolated, not a directly tested point.
WHY THE OBSERVED RATE DEFICIT IS SMALLER THAN THE BLACKHOLE FRACTION
The blackhole covers the stated fraction of the window after an eight-second warm-up, while the measured window also contains that warm-up and the restore tail. A 75 % blackhole therefore yields a ratio of 0.37 rather than 0.25.
Sampling limit
Levels were drawn at random rather than swept, so replicate counts are uneven and the decisive missed level rests on a single run. The 55 % level offered by the design was never drawn; window arithmetic predicts a ratio near 0.57, which would also have evaded.
Notes: Worklet mapping: M6 measured detection boundary. Presenting the boundary is more informative than presenting 11/12 alone: it tells an operator the evasion condition rather than a bare miss rate. Because 55 % was never drawn and would also have evaded, recall against the full designed parameter space is weaker than 11/12 implies. This is stated rather than left to be discovered. Short or bursty interception that averages out across the window is not detected by a rate-based clause; a continuity-based clause is proposed in the remaining-work slide.

## Slide 27
UNRESOLVED CASES
Experimentally Verified Limitations
Each limitation is stated with the evidence that established it, the technical reason, and its implication | All figures recomputed from the 168-run corrected campaign
OBSERVED LIMITATION
EVIDENCE
TECHNICAL REASON
IMPLICATION
Planned boundary-clock replacement is classified as an attack
0/12 runs
The provisioned context holds a single expected boundary-clock identity, so a legitimate replacement relay is indistinguishable from an unauthorised one.
Produces 12 false ATTACK calls and dominates the 0.783 specificity. Excluding it, benign classification is 47/48 = 0.979.
Sustained interception below roughly 60 % evades detection
1 of 12 C1 runs
The rate-starvation clause fires below a 0.500 delivered-to-declared ratio; a 60 % blackhole yields 0.5049 and stays above it.
An attacker who paces interception under the threshold is not detected by a rate-based clause alone.
Coherent GNSS spoofing is not establishable here
testbed limit
Downstream PTP telemetry cannot separate a perfectly-mimicking spoof from a healthy clock; receiver RF observables, multi-antenna geometry or an independent time anchor are required.
No claim is made about GNSS spoof detection. The limit is on PTP-layer features, not on software in general.
Held-out evidence is small and partly incomplete
4 per scenario
Only four held-out replicates exist per scenario, and 48 of 168 runs lack pmc management telemetry.
Confidence intervals are wide by construction, and the ML arm sees 6 of 28 configured features.
Replicate metadata is internally inconsistent
36 runs
Thirty-six C-series context files record replicate 901 rather than their true replicate number.
The evaluation uses the replicate encoded in the directory name. This must be corrected before any fresh validation claim.
Each limitation is an experimental finding with a located cause, not a residual uncertainty. Four of the five have a defined software or hardware route to resolution, set out on the following slides.
Notes: Worklet mapping: M6 documented limitations. Volunteering these is deliberate. A reviewer who discovers an undisclosed limitation will discount the remainder of the evidence. The B3 congestion miss is not listed as a separate limitation because it is an abstention rather than a misclassification, but it is the second contributor to the 0.783 specificity and is stated on the results slide.

## Slide 28
WORKLET STATUS
Delivery Status and Objectives Not Yet Addressed
Status assessed against the original worklet milestone plan | Objective numbering follows the worklet definition reproduced on the opening slide
DONE
PARTIAL
NOT STARTED
M1
Problem study and literature survey
Standards baseline, reviewed source set, documented gap
DONE
M1
System architecture design
Data flow defined: capture, extract, decide
DONE
M2
KPI and fault taxonomy
144-parameter × 16-fault matrix; profile configuration traced to standards
DONE
M3
Digital twin and fault injection
Six-node testbed and live injection validated; digital twin not exercised
PARTIAL
M4
AI model development
Random Forest and Isolation Forest evaluated; not usable on available telemetry
PARTIAL
M5
Healing logic integration
Decision engine evaluated; closed-loop healing not validated
PARTIAL
M6a
Testing and evaluation
168-run campaign plus rule-versus-ML comparison
DONE
M6b
Paper and IP draft
Publication and patent disclosure
NOT STARTED
WORKLET OBJECTIVES NOT YET ADDRESSED
1
Fault prediction
Prediction before service disruption was not attempted in this campaign.
2
Automated corrective action
No corrective action was executed or measured. ISOLATE, HOLDOVER and ESCALATE are verdict outputs, not actions taken.
3
Digital-twin validation
The digital twin was not exercised; fault injection ran directly on the testbed.
4
Outcome metrics
No MTTR, recovery-time, availability or downtime figure was measured on this testbed.
Next gate
The missing objectives must be executed and their recovery outcomes measured before any self-healing claim is made. The work reported here establishes detection and classification, which is the prerequisite for them.
Notes: Worklet mapping: delivery status against the original milestone plan. Worklet objectives 1, 3 and 5 are addressed: anomaly detection is delivered by the rule engine, the testbed provides controlled fault injection, and the AI-versus-rule comparison is complete with a statistical control. Objectives 2 and 4 are not addressed in this sub-scope, and the expected outcomes concerning faster recovery and improved availability were not measured here. This is stated rather than inferred.

## Slide 29
RESOLUTION PLAN
Remaining Work: Software and Hardware
Software items are actionable on the existing testbed | Hardware items require equipment not present in a software-only environment | Each item maps to a limitation stated on the preceding slides
SOFTWARE — ACTIONABLE IMMEDIATELY
Provisioned replacement context
Extend the operator context to carry approved replacement boundary-clock identities, then re-freeze and re-run. Closes the 0/12 benign failure and is expected to raise specificity toward 0.979.
Finer interception sweep
Test levels between 55 % and 65 % as a sweep rather than a random draw, to replace the interpolated 60.5 % crossing with a measured one.
Continuity-based detection
Add a clause that tracks message-arrival continuity alongside average rate, so that paced or bursty interception below the rate threshold is still detected.
Richer telemetry for the ML arm
Supply management-plane telemetry in addition to servo logs and repeat the comparison, so the ML arm is evaluated on adequate observability.
Metadata and re-freeze
Correct the 36 inconsistent replicate identifiers, re-hash the revised rule, and re-run the campaign for an independently pre-registered result.
HARDWARE — REQUIRES EQUIPMENT
GNSS receiver
Unlocks GNSS spoofing (A6), GNSS jamming (A7) and genuine holdover (B1) — three of the five currently unreachable classes.
Second physical machine
Provides a second independent oscillator, making oscillator drift (B6) reproducible. Clocks in one host cannot genuinely drift apart.
Hardware-timestamping NIC
Replaces microsecond-scale software timestamping with nanosecond-scale hardware timestamping, enabling credible physical-impact measurement for the delay attack (A4) and static asymmetry (B5).
SyncE-capable PHY
Unlocks SyncE and EEC degradation (B4). SyncE is a physical-layer function and veth interfaces have no PHY, so ESMC quality signalling cannot exist in this testbed.
Five of sixteen catalogued classes require hardware; three more have software detection logic but need hardware for credible physical-impact measurement. The software items above are unblocked and can begin on the existing testbed.
Notes: Worklet mapping: M3, M5 and M6 remaining work. Hardware priority order if procurement is limited: a GNSS receiver unlocks three classes and is the single highest-value item; a hardware-timestamping NIC improves the credibility of every timing-magnitude claim; a second machine and a SyncE PHY unlock one class each. The software items are ordered by expected effect on the reported metrics: the provisioned-replacement fix addresses the only systematic benign failure.

## Slide 30
TECHNICAL SUMMARY
Open Fronthaul S-Plane Timing Security
1
Scope investigated
Discrimination of malicious timing behaviour from benign timing faults on the Open Fronthaul S-plane, between O-DU and O-RU.
2
Implementation
Six linuxptp 4.0 daemons under the ITU-T G.8275.1 telecom profile across two bridged segments, with faults produced on the live packet path.
3
Dataset produced
168 live runs across 14 scenarios at 12 randomised replicates each; 1,451,909 packet records extracted at 56 fields per packet, with unobservable fields recorded EMPTY.
4
Taxonomy evaluated
Eight attack scenarios, five benign scenarios and one deliberately ambiguous case, drawn from a sixteen-class catalogue of which eight were executable in software.
5
Classification performance
Macro attack sensitivity 0.990 for the revised rule against 0.625 pre-frozen; specificity 0.783, or 0.979 excluding the identified benign failure; abstention 12/12; attribution 0.875.
6
Comparison outcome
On 56 held-out runs the rule arm reached 0.911 against 0.429 for the ML arm and 0.357 for a constant predictor; the ML arm is not statistically distinguishable from that control on the available telemetry.
7
Limits identified
One systematic benign failure with a defined fix, an interception evasion band near 60 %, and five fault classes requiring hardware.
8
Immediate next steps
Extend the provisioned-replacement context and re-freeze; sweep interception levels; add continuity-based detection; re-run the ML arm with management-plane telemetry.
Thank you
Tanmaya Kumar · Raghu Ram K · Munipalle Jaswanth Kumar
Status: S-plane detection and classification evaluated. Prediction, digital twin and automated healing not yet executed.
Notes: Worklet mapping: closing technical summary. No new claim is introduced on this slide; every figure appears earlier with its evidence. If asked for the single most important caveat: the 0.990 sensitivity belongs to a rule revised after observing the campaign, and the pre-frozen rule scored 0.625 on the same captures. Both figures are reported throughout.